## Slide 1: Routing Studio Examples
For ATD Advanced Routing Environment

## Slide 2: Overview
Enterprise Routing
EVPN Services
L3LS
Campus
Studios Used
These slides contain examples and instructions of how to build end to end topologies with and services in Cloud Vision Studios. Featured is the Enterprise Routing Studio that is used to connect Campus and DCs together.
Arista Avanced Routing ATDs are used for these examples because they supply an easy environment for getting familiar with the interop between Studios that is required to configure complete networks.
Topologies Covered
DC to DC L2EVPN
DC to DC L3EVPN + eBGP
Campus to ISP
Campus to Campus Routed
Campus to Campus L2 stretch L2EVPN
Enterprise OSPF on DC Border Leaf

## Slide 3: Files to Run the Examples
Enterprise Routing Studio is also found in this repository and must be loaded to the ATD until it is a built-in in the CV version in the ATD (Kent)
All Files found here:
https://github.com/arista-netdevops-community/CloudVisionPortal-Examples/tree/master/CloudVision_Studios/Enterprise%20Routing%20Studio%20Examples
Note: The interface configuration built-in studio has a bug, please use the fixed version found in the above repository
Download the inputs files to your laptop

## Slide 5: Launch the Advanced Routing ATD

## Slide 6: Complete Topology of the ATD
We will be using a sub-set of this topology for each Enterprise Routing Studio example

## Slide 7: Enable Export/Import of Studios data files This is an Alpha feature and needs to be enabled in Jackson; the current ATD release. This allows the example files that go with these slides to be loaded.

## Slide 8: Import Enterprise Routing Studio into ATD
Once Kent version of CV is released this step is not needed because the Enterprise Routing will be a "Built-In Studio".
File location:
https://github.com/arista-netdevops-community/CloudVisionPortal-Examples/tree/master/CloudVision_Studios/Enterprise%20Routing

## Slide 9: Import the Inputs for each Studio for each example
These files should be on your laptop
All Files found here:
https://github.com/arista-netdevops-community/CloudVisionPortal-Examples/tree/master/CloudVision_Studios/Enterprise%20Routing%20Studio%20Examples
Note: The interface configuration built-in studio has a bug, please use the fixed version found in the above repository

## Slide 10: Note: submit workspace if upgrading to Kent this adds the new Studio

## Slide 11
L3LS Studio and Enterprise Routing Studio will set ASN tags. The user does not need to create them.
L3LS Studio will set these lo0/router ID Tags. The user must create them in the Enterprise Routing Studio if using ISIS or EVPN.

## Slide 12: Other Notes
Be sure to accept "updates" in the Inventory and Topology Studio prior to Selecting devices in each Studio
Be sure to check that the drop down fields in EVPN Services and Inventory Studio are populated – Jackson release had a problen with this
When changing between example be sure to clear the arp cache in the end devices prior to sending a ping – the mac of the gw may have changed
Use the version of Interface Studio on the github site – it fixes a bug where when changing from a routed port to bridged port is missing the "switchport" command
Both the router_bgp.as Tag and the router_bgp.router_id Tag (for lo0) are written by the L3LS Studio and do not have to be entered by the user. If Enterprise Routing Studio has EVPN/VXLAN enabled the router_bgp.router_id (lo0) tag must be added
Tag Role:Edge-Router is only available in CV version Kent and beyond. If using Jackson release please ignore this tag

## Slide 13: Example 1 Routing between DCs with L2EVPN
Studios
Enterprise Routing
EVPN Services
L3LS

## Slide 14: Example1: Routing Between 2 Data Centers L2 EVPN and L3 Edge on Enterprise Routers
In this example the Enterprise Routing Studio, consisting of a Core Router and 2 Edge Routers, connects 2 DC together
The DC border leafs have a trunk port to Edge Router and another leaf has a trunk to the end device
A vlan in 1 DC containing the end device is routed to a different vlan in another DC
Each vlan is a L2 EVPN in Each DC with the end device and the Edge Router in the VPN.
The Edge Router is the default gw for end devices in each DC. (A switch is used for the end device to launch pings from)
Example2 and example3 build on example 1

## Slide 15: Example1 Routing Between 2 DCs, L2EVPN in each DC

## Slide 16: Example1 Tags
 | eos1 | eos2 | eos5 | eos6 | eos14 | eos8 | eos3 | eos4 | eos9 | eos18 | eos20
Network Tag | Network:CoreNet | Network:CoreNet | Network:CoreNet |  |  |  |  |  |  | Network:DC14-6-8End-device | Network:DC9-3-4End-device
Role Tag | Role:Edge-Router | Role:Core | Role:Edge-Router | Role:Leaf | Role:Spine | Role:Leaf | Role:Leaf | Role:Leaf | Role:Spine | Role:Edge-Router | Role:Edge-Router
Edge Router Domain Tag | Edge-Router-Domain:1 |  | Edge-Router-Domain:5 |  |  |  |  |  |  | Edge-Router-Domain:18 | Edge-Router-Domain:20
DC Tag |  |  |  | DC:14-6-8 | DC:14-6-8 | DC:14-6-8 | DC:9-4-3 | DC:9-4-3 | DC:9-4-3 |  | 
DC-Pod Tag |  |  |  | DC-Pod:1 | DC-Pod:1 | DC-Pod:1 | DC-Pod:2 | DC-Pod:2 | DC-Pod:2 |  | 
Leaf Domain |  |  |  | Leaf-Domain:1 |  | Leaf-Domain:2 | Leaf-Domain:3 | Leaf-Domain:4 |  |  | 
Number |  |  |  | Leaf-Number:1 | Spine-Number:1 | Leaf-Number:2 | Leaf-Number:1 | Leaf-Number:2 | Spine-Number:1 |  | 

## Slide 18: TAGs for example 1
eos1
eos2
eos5
eos3
eos4
eos9
eos6
eos14
eos8
eos20
eos18

## Slide 19: Device Selection

## Slide 20: Test
From eos18 ping eos20 14.14.14.2

## Slide 21: Example 2 Routing between DCs L3EVPN
Studios
Enterprise Routing
EVPN Services
L3LS

## Slide 22: Example2: Routing Between 2 Data Centers L3EVPN and eBGP from Border Leaf to Enterprise Router
In this example the Enterprise Routing Studio, consisting of a Core Router and 2 Edge Routers, connects 2 DC together
The DC border leafs have a trunk port to Edge Router and another leaf has a trunk to the end device
A vlan in 1 DC containing the end device is routed to a different vlan in another DC
Each vlan is a L3 EVPN in Each DC with the end device and the Edge Router in the VPN.
The Edge Router is the default gw for end devices in each DC. (A switch is used for the end device to ping from)
Ping from eos18 13.13.13.2/24 to eos 20 14.14.14.2/24

## Slide 23: Example2 Routing Between 2 DCs, L3EVPN in each DC

## Slide 24: Example 2 Tags
 | eos1 | eos2 | eos5 | eos6 | eos14 | eos8 | eos3 | eos4 | eos9 | eos18 | eos20
Network Tag | Network:CoreNet | Network:CoreNet | Network:CoreNet | Network:DC14-6-8Border-Leaf |  |  |  | Network:DC9-3-4Border-Leaf |  | Network:DC14-6-8End-device | Network:DC9-3-4End-device
Role Tag | Role:Edge-Router | Role:Core | Role:Edge-Router | Role:Edge-Router | Role:Spine | Role:Leaf | Role:Leaf | Role:Edge-Router | Role:Spine | Role:Edge-Router | Role:Edge-Router
Other Role Tag |  |  |  | Role:Leaf |  |  |  | Role:Leaf |  |  | 
Edge Router Domain Tag | Edge-Router-Domain:1 |  | Edge-Router-Domain:5 | Edge-Router-Domain:6 |  |  |  | Edge-Router-Domain:4 |  | Edge-Router-Domain:18 | Edge-Router-Domain:20
DC Tag |  |  |  | DC:14-6-8 | DC:14-6-8 | DC:14-6-8 | DC:9-4-3 | DC:9-4-3 | DC:9-4-3 |  | 
DC Pod Tag |  |  |  | DC-Pod:1 | DC-Pod:1 | DC-Pod:1 | DC-Pod:2 | DC-Pod:2 | DC-Pod:2 |  | 
Leaf Domain |  |  |  | Leaf-Domain:1 |  | Leaf-Domain:2 | Leaf-Domain:3 | Leaf-Domain:4 |  |  | 
Number |  |  |  | Leaf-Number:1 | Spine-Number:1 | Leaf-Number:2 | Leaf-Number:1 | Leaf-Number:2 | Spine-Number:1 |  | 

## Slide 26: TAGs for example 2 – the DC border routers have additional tags from the previous example
eos1
eos2
eos5
eos3
eos4
eos9
eos6
eos14
eos8
eos20
eos18

## Slide 27: Device Selection

## Slide 28: Test
From eos18 ping eos20 14.14.14.2
You may have to clear the arp cache on eos18 between the mac address of its default gateway has changed from the previous example

## Slide 29: Example 3
Studios
Enterprise Routing
EVPN Services
L3LS

## Slide 30: Example3: L3EVPN on CoreNet
In this example the Enterprise Routing Studio is configured to put the traffic in an L3EVPN between the DCs and over a 3rd L3EVPN segment in the Enterprise Core
The border leafs have eBGP sessions to the Edge Routers and the interface on the Edge Router side is in a VRF.
Clone the EVPN Services Studio – it will be used for the EVPN over the Enterprise Core Network. This will avoid the limitation of a vlan id cannot be reused even if it is on a different network (vlan between border leafs and edge router for example)

## Slide 31
Example3: L3EVPN on CoreNet

## Slide 32: Tags
 | eos1 | eos2 | eos5 | eos6 | eos14 | eos8 | eos3 | eos4 | eos9 | eos18 | eos20 | eos17
Network Tag | Network:CoreNet | Network:CoreNet | Network:CoreNet | Network:DC14-6-8Border-Leaf |  |  |  | Network:DC9-3-4Border-Leaf |  | Network:DC14-6-8End-device | Network:DC9-3-4End-device | Network:CoreNet
Role Tag | Role:Edge-Router | Role:Core | Role:Edge-Router | Role:Edge-Router | Role:Spine | Role:Leaf | Role:Leaf | Role:Edge-Router | Role:Spine | Role:Edge-Router | Role:Edge-Router | Role:RR
Other Role Tag |  |  |  | Role:Leaf |  |  |  | Role:Leaf |  |  |  | 
Edge Router Domain Tag | Edge-Router-Domain:1 |  | Edge-Router-Domain:5 | Edge-Router-Domain:6 |  |  |  | Edge-Router-Domain:4 |  | Edge-Router-Domain:18 | Edge-Router-Domain:20 | 
Lo0 Tag | router_bgp.router_id:1.1.1.1 |  | router_bgp.router_id:5.5.5.5 |  |  |  |  |  |  |  |  | router_bgp.router_id:17.17.17.17
DC Tag |  |  |  | DC:14-6-8 | DC:14-6-8 | DC:14-6-8 | DC:9-4-3 | DC:9-4-3 | DC:9-4-3 |  |  | 
DC Pod Tag |  |  |  | DC-Pod:1 | DC-Pod:1 | DC-Pod:1 | DC-Pod:2 | DC-Pod:2 | DC-Pod:2 |  |  | 
Leaf Domain |  |  |  | Leaf-Domain:1 |  | Leaf-Domain:2 | Leaf-Domain:3 | Leaf-Domain:4 |  |  |  | 
Number |  |  |  | Leaf-Number:1 | Spine-Number:1 | Leaf-Number:2 | Leaf-Number:1 | Leaf-Number:2 | Spine-Number:1 |  |  | 

## Slide 34: Device Selection
Clone the EVPN Services Studio. This clone will be used for the EVPN over the Enterprise Core Network

## Slide 35: Test
From eos18 ping eos20 14.14.14.2
You may have to clear the arp cache on eos18 between the mac address of its default gateway has changed from the previous example

## Slide 36: Example 4
Studios
Enterprise Routing
Campus

## Slide 37: Example4: Routing OSPF Campus and eBGP to ISP Campus receives Default Route Campus edge router has full Internet routes
In this example the Enterprise Routing Studio, consisting of 3 Edge Routers route a Campus to the Internet
ISP sends full routes but Edge Router sends only a default route to the Campus Splines
Ping from Campus switch eos12 15.15.15.4/24 to eos10 on ISP network 10.10.10.10

## Slide 38
Example4: Routing OSPF Campus and eBGP to ISP

## Slide 39: Example 4 Tags
 | eos1 | eos7 | eos10 | eos11 | eos12 | eos13 | eos19
Network Tag | Network:CoreNet | Network:ISP | Network:ISP | Network:CoreNet |  | Network:CoreNet | Network:ISP
Role Tag | Role:Edge-Router | Role:Edge-Router | Role:Core | Role:Edge-Router |  | Role:Edge-Router | Role:Core
Roter ID Tag |  | router_bgp.router_id:7.7.7.7 | router_bgp.router_id:10.10.10.10 |  |  |  | router_bgp.router_id:19.19.19.19
Campus Tag |  |  |  | Campus:Campus11-12-13 | Campus:Campus11-12-13 | Campus:Campus11-12-13 | 
Campus Pod Tag |  |  |  |  | Campus-Pod:12 |  | 

## Slide 41: Device Selection

## Slide 42: Test
From Campus switch eos12 ping to eos10 on the ISP network 10.10.10.10

## Slide 43: Example 5
Studios
Enterprise Routing
Campus
EVPN Services

## Slide 44: Example5: Routing OSPF Campus to Campus + L2 vlan stretch between Campus
In this example the Enterprise Routing Studio, consisting of 3 Edge Routers route a Campus to the Internet
ISP sends full routes but Edge Router sends only a default route to the Campus Splines
Ping from Campus switch eos12 15.15.15.4/24 to eos10 on ISP network 10.10.10.10

## Slide 45
Example5: Routing OSPF Campus to Campus

## Slide 46: Example 5 Tags
 | eos1 | eos2 | eos5 | eos7 | eos10 | eos11 | eos12 | eos13 | eos19 | eos3 | eos20 | eos4 | eos17 | eos9
Network Tag | Network:CoreNet | Network:CoreNet | Network:CoreNet | Network:ISP | Network:ISP | Network:CoreNet |  | Network:CoreNet | Network:ISP |  | Network:Campus2-5-3-4EndDevice3 |  | Network:CoreNet | Network:Campus2-5-3-4EndDevice4
Role Tag | Role:Core | Role:Edge-Router | Role:Edge-Router | Role:Edge-Router | Role:Core | Role:Edge-Router |  | Role:Edge-Router | Role:Core |  | Role:Edge-Router |  | Role:RR | Role:Edge-Router
Edge Router Domain Tag |  | Edge-Router-Domain:Campus2-5-3-4 | Edge-Router-Domain:Campus2-5-3-4 | Edge-Router-Domain:7 |  | Edge-Router-Domain:Campus11-12-13 |  | Edge-Router-Domain:Campus11-12-13 |  |  | Edge-Router-Domain:20 |  |  | Edge-Router-Domain:9
Router ID Tag (lo0) |  | router_bgp.router_id:2.2.2.2 | router_bgp.router_id:5.5.5.5 | router_bgp.router_id:7.7.7.7 | router_bgp.router_id:10.10.10.10 | router_bgp.router_id:11.11.11.11 |  | router_bgp.router_id:13.13.13.13 | router_bgp.router_id:19.19.19.19 |  |  |  | router_bgp.router_id:17.17.17.17 | 
Campus Tag |  | Campus:Campus2-5-3-4 | Campus:Campus2-5-3-4 |  |  | Campus:Campus11-12-13 | Campus:Campus11-12-13 | Campus:Campus11-12-13 |  | Campus:Campus2-5-3-4 |  | Campus:Campus2-5-3-4 |  | 
Campus Pod Tag |  |  |  |  |  |  | Campus-Pod:12 |  |  | Campus-Pod:3 |  | Campus-Pod:4 |  | 

## Slide 48: Device Selection

## Slide 49: Test
From Campus switch eos12 ping DC end device eos9 15.15.15.2
From Campus switch eos12 ping to eos10 on the ISP network 10.10.10.10
From DC end device ping eos10 on ISP network 10.10.10.10

## Slide 50: Example 6
Studios
Enterprise Routing
Campus
L3LS

## Slide 51: Example6: L2DC to L3 DC L3 DC has no overlay and runs OSPF on Border Leafs
In this example the Enterprise Routing Studio, consisting of 4 Edge Routers and 2 Core Routers routes a L3DC using L3LS Studio to an L2 DC using the Campus Studio.
On the border leafs on the L3 DC BGP to OSPF redistribution is configured using the Enterprise Routing Studio

## Slide 52
Example6: L2DC to L3 DC

## Slide 53: Example 6Tags
 | eos1 | eos6 | eos12 | eos11 | eos13 | eos2 | eos5 | eos3 | eos4 | eos9
Network Tags | Network:CoreNet | Network:CoreNet |  | Network:CoreNet | Network:CoreNet | Network:CoreNet | Network:CoreNet |  |  | Network:L3EVPN-DC-End-device
Role Tags | Role:Core | Role:Core |  | Role:Edge-Router | Role:Edge-Router | Role:Edge-Router | Role:Edge-Router | Role:Spine | Role:Spine | Role:Edge-Router
Other Role Tags |  |  |  |  |  | Role:Leaf | Role:Leaf |  |  | Role:Leaf
Edge Router Domain Tags |  |  |  | Edge-Router-Domain:11-13 | Edge-Router-Domain:11-13 | Edge-Router-Domain:2 | Edge-Router-Domain:5 |  |  | Edge-Router-Domain:9
DC Tags |  |  |  |  |  | DC:L3DC DC-Pod:1 | DC:L3DC DC-Pod:1 | DC:L3DC DC-Pod:1 | DC:L3DC DC-Pod:1 | DC:L3DC DC-Pod:1
Leaf Domain Tags |  |  |  |  |  | Leaf-Domain:2 | Leaf-Domain:5 |  |  | Leaf-Domain:9
Number Tags |  |  |  |  |  | Leaf-Number:1 | Leaf-Number:5 | Spine-Number:1 | Spine-Number:2 | Leaf-Number:9
Campus Tags |  |  | Campus:L2DC | Campus:L2DC | Campus:L2DC |  |  |  |  | Campus:L3EVPN-DC-End-device
Campus Pod Tags |  |  | Campus-Pod:Leaf1 |  |  |  |  |  |  | 

## Slide 55: Device Selection

## Slide 56: Test
From Campus switch eos12 ping DC Leaf eos9 14.14.14.2

## Slide 57: Example 7
Studios
Enterprise Routing
Campus
L3LS

## Slide 58: Example7: BGP Routing DC to Core to Campus Border Leafs and Campus Splines connect eBGP to Enterprise Core
In this example the Enterprise Routing Studio, consisting of 2 Edge Routers in a Camus, 2 Core Routers and 2 Edge Routers in L3DC

## Slide 59
Example7: BGP Routed Enterprise

## Slide 60: Example 7 Tags
 | eos1 | eos6 | eos12 | eos11 | eos13 | eos2 | eos5 | eos3 | eos4 | eos9
Network Tags | Network:CoreNet | Network:CoreNet |  | Network:L2DC | Network:L2DC | Network:L3DC | Network:L3DC |  |  | Network:L3EVPN-DC-End-device
Role Tags | Role:Core | Role:Core |  | Role:Edge-Router | Role:Edge-Router | Role:Edge-Router | Role:Edge-Router |  |  | Role:Edge-Router
Other Role Tags |  |  |  |  |  | Role:Leaf | Role:Leaf | Role:Spine | Role:Spine | Role:Leaf
Edge Router Domain Tags |  |  |  | Edge-Router-Domain:11-13 | Edge-Router-Domain:11-13 | Edge-Router-Domain:2 | Edge-Router-Domain:5 |  |  | Edge-Router-Domain:9
DC Tags |  |  |  |  |  | DC:L3DC DC-Pod:1 | DC:L3DC DC-Pod:1 | DC:L3DC DC-Pod:1 | DC:L3DC DC-Pod:1 | DC:L3DC DC-Pod:1
Leaf Domain |  |  |  |  |  | Leaf-Domain:2 | Leaf-Domain:5 |  |  | Leaf-Domain:9
Number Tags |  |  |  |  |  | Leaf-Number:1 | Leaf-Number:5 | Spine-Number:1 | Spine-Number:2 | Leaf-Number:9
Campus Tags |  |  | Campus:L2DC | Campus:L2DC | Campus:L2DC |  |  |  |  | Campus:L3EVPN-DC-End-device
Campus Pod Tags |  |  | Campus-Pod:Leaf1 |  |  |  |  |  |  | 

## Slide 62: Device Selection

## Slide 63: Test
From Campus switch eos12 ping DC Leaf eos9 14.14.14.2