## Slide 1: Studios Interop
For ATD Advanced Routing Environment
Brian Hayes

## Slide 2: Overview
Enterprise Routing
EVPN Services
L3LS
Campus
Studios Used
These slides contain examples and instructions of how to build end to end topologies with and services in Cloud Vision Studios. Featured is the Enterprise Routing Studio that is used to connect Campus and DCs together.
Arista Avanced Routing ATDs are used for these examples because they supply an easy environment for getting familiar with the interop between Studios that is required to configure complete networks.
Topologies Covered
DC to DC L2EVPN
DC to DC L3EVPN + eBGP
Campus to ISP
Campus to Campus Routed
Campus to Campus L2 stretch L2EVPN
Enterprise OSPF on DC Border Leaf
VRF Lite

## Slide 3: Files to Run the Examples
Enterprise Routing Studio is also found in this repository and must be loaded to the ATD until it is a built-in in the CV version in the ATD (Kent)
All Files found here:
https://github.com/arista-netdevops-community/CloudVisionPortal-Examples/tree/master/CloudVision_Studios/Enterprise%20Routing%20Studio%20Examples
Note: The interface configuration built-in studio has a bug, please use the fixed version found in the above repository
Download the Studios Inputs files to your laptop

## Slide 4: Directories with the Inputs Files for each example

## Slide 5: Launch the Advanced Routing ATD
https://testdrive.arista.com/

## Slide 6: Complete Topology of the ATD
We will be using a sub-set of this topology for each Enterprise Routing Studio example

## Slide 7: Enable Export/Import of Studios data files This is an Alpha feature and needs to be enabled in the current ATD release. This allows the example files that go with these slides to be loaded.

## Slide 8: Import Enterprise Routing Studio into ATD
Once Kent version of CV is released this step is not needed because the Enterprise Routing will be a "Built-In Studio".
File location:
https://github.com/arista-netdevops-community/CloudVisionPortal-Examples/tree/master/CloudVision_Studios/Enterprise%20Routing

## Slide 9: Import the Inputs for each Studio for each example
These files should be on your laptop
All Files found here:
https://github.com/arista-netdevops-community/CloudVisionPortal-Examples/tree/master/CloudVision_Studios/Enterprise%20Routing%20Studio%20Examples
Note: The interface configuration built-in studio has a bug, please use the fixed version found in the above repository

## Slide 10: If upgrading CV, new Studios are in a workspace when the upgrade completes Submitting this workspace adds the new Studio permentently

## Slide 11: Note: Some Tags are created automatically by Studios not by users
L3LS Studio and Enterprise Routing Studio will set ASN tags. The user does not need to create them.
L3LS Studio will set these lo0/router ID Tags. The user must create them in the Enterprise Routing Studio if using ISIS or EVPN.

## Slide 12: Other Notes
Be sure to accept "updates" in the Inventory and Topology Studio prior to Selecting devices in each Studio
Be sure to check that the drop down fields in EVPN Services and Inventory Studio are populated – Jackson release had a problem with this
When changing between example be sure to clear the arp cache in the end devices prior to sending a ping – the mac of the gw may have changed
Use the version of Interface Studio on the github site – it fixes a bug where when changing from a routed port to bridged port is missing the "switchport" command
Both the router_bgp.as Tag and the router_bgp.router_id Tag (for lo0) are written by the L3LS Studio and do not have to be entered by the user. If Enterprise Routing Studio has EVPN/VXLAN enabled the router_bgp.router_id (lo0) tag must be added
Tag Role:Edge-Router is only available in CV version Kent and beyond. If using Jackson release please ignore this tag

## Slide 13: Example 1 DC Gateway Router

## Slide 14: Example1: DC Gateway Router This example also routes between DCs with OSPF
In this example the Enterprise Routing Studio, consisting of a Core Router and 2 Edge Routers, connects 2 DC together
The DC border leafs have a trunk port to Edge Router and another leaf has a trunk to the end device
A vlan in 1 DC containing the end device is routed to a different vlan in another DC
Each vlan is a L2 EVPN in Each DC with the end device and the Edge Router in the VPN.
The Edge Router is the default gw for end devices in each DC. (A switch is used for the end device to launch pings from)
Example2 and example3 build on example 1

## Slide 15: Example1

## Slide 16: Example1 Tags
See tagsfile.txt to load tags through the API with tagman.py
DC-Pod:1 - EOS14
DC-Pod:1 - EOS6
DC-Pod:1 - EOS8
DC-Pod:2 - EOS3
DC-Pod:2 - EOS4
DC-Pod:2 - EOS9
DC:DC-eos3-eos4-eos9 - EOS3
DC:DC-eos3-eos4-eos9 - EOS4
DC:DC-eos3-eos4-eos9 - EOS9
DC:DC-eos6-eos8-eos14 - EOS14
DC:DC-eos6-eos8-eos14 - EOS6
DC:DC-eos6-eos8-eos14 - EOS8
Edge-Router-Domain:1 - EOS1
Edge-Router-Domain:18 - EOS18
Edge-Router-Domain:20 - EOS20
Edge-Router-Domain:5 - EOS5
Leaf-Domain:1 - EOS6
Leaf-Domain:2 - EOS8
Leaf-Domain:3 - EOS3
Leaf-Domain:4 - EOS4
Leaf-Number:1 - EOS4
Leaf-Number:1 - EOS6
Leaf-Number:2 - EOS3
Leaf-Number:2 - EOS8
Network:CoreNet-eos1-eos2-eos5 - EOS1
Network:CoreNet-eos1-eos2-eos5 - EOS2
Network:CoreNet-eos1-eos2-eos5 - EOS5
Network:DC-End-device-eos18 - EOS18
Network:DC-End-device-eos20 - EOS20
Role:Core - EOS2
Role:Edge-Router - EOS1
Role:Edge-Router - EOS5
Role:Leaf - EOS3
Role:Leaf - EOS4
Role:Leaf - EOS6
Role:Leaf - EOS8
Role:Spine - EOS14
Role:Spine - EOS9
Spine-Number:1 - EOS14
Spine-Number:1 - EOS9
router_bgp.router_id:1.1.1.1 - EOS1
router_bgp.router_id:2.2.2.2 - EOS2
router_bgp.router_id:5.5.5.5 - EOS5

## Slide 17: Device Selection

## Slide 18: Test
From eos18 ping eos20 14.14.14.2

## Slide 19: Example 2 Routing eBGP between DCs eBGP between border Leaf and Edge Router

## Slide 20: Example2: Routing Between 2 Data Centers L3EVPN and eBGP from Border Leaf to Enterprise Router
In this example the Enterprise Routing Studio, consisting of a Core Router and 2 Edge Routers, connects 2 DC together
The DC border leafs have a trunk port to Edge Router and another leaf has a trunk to the end device
A vlan in 1 DC containing the end device is routed to a different vlan in another DC
Each vlan is a L3 EVPN in Each DC with the end device and the Edge Router in the VPN.
The Edge Router is the default gw for end devices in each DC. (A switch is used for the end device to ping from)
Ping from eos18 13.13.13.2/24 to eos 20 14.14.14.2/24

## Slide 21: Example2

## Slide 22: Example 2 Tags
See tagsfile.txt to load tags through the API with tagman.py
DC-Pod:1 - EOS14
DC-Pod:1 - EOS6
DC-Pod:1 - EOS8
DC-Pod:2 - EOS3
DC-Pod:2 - EOS4
DC-Pod:2 - EOS9
DC:DC-eos3-eos4-eos9 - EOS3
DC:DC-eos3-eos4-eos9 - EOS4
DC:DC-eos3-eos4-eos9 - EOS9
DC:DC-eos6-eos8-eos14 - EOS14
DC:DC-eos6-eos8-eos14 - EOS6
DC:DC-eos6-eos8-eos14 - EOS8
Edge-Router-Domain:1 - EOS1
Edge-Router-Domain:18 - EOS18
Edge-Router-Domain:20 - EOS20
Edge-Router-Domain:4 - EOS4
Edge-Router-Domain:5 - EOS5
Edge-Router-Domain:6 - EOS6
Leaf-Domain:1 - EOS6
Leaf-Domain:2 - EOS8
Leaf-Domain:3 - EOS3
Leaf-Domain:4 - EOS4
Leaf-Number:1 - EOS4
Leaf-Number:1 - EOS6
Leaf-Number:2 - EOS3
Leaf-Number:2 - EOS8
Network:CoreNet-eos1-eos2-eos5 - EOS1
Network:CoreNet-eos1-eos2-eos5 - EOS2
Network:CoreNet-eos1-eos2-eos5 - EOS5
Network:DC-Border-Leaf-eos4 - EOS4
Network:DC-Border-Leaf-eos6 - EOS6
Network:DC-End-device-eos18 - EOS18
Network:DC-End-device-eos20 - EOS20
Role:Core - EOS2
Role:Edge-Router - EOS1
Role:Edge-Router - EOS5
Role:Leaf - EOS3
Role:Leaf - EOS4
Role:Leaf - EOS6
Role:Leaf - EOS8
Role:Spine - EOS14
Role:Spine - EOS9
Spine-Number:1 - EOS14
Spine-Number:1 - EOS9
router_bgp.router_id:1.1.1.1 - EOS1
router_bgp.router_id:2.2.2.2 - EOS2
router_bgp.router_id:5.5.5.5 - EOS5

## Slide 23: Device Selection

## Slide 24: Test
From eos18 ping eos20 14.14.14.2
You may have to clear the arp cache on eos18 between the mac address of its default gateway has changed from the previous example

## Slide 25: Example 3 EVPN on Enterprise Core

## Slide 26: Example3: L3EVPN on CoreNet
In this example the Enterprise Routing Studio is configured to put the traffic in an L3EVPN between the DCs and over a 3rd L3EVPN segment in the Enterprise Core
The border leafs have eBGP sessions to the Edge Routers and the interface on the Edge Router side is in a VRF.
Clone the EVPN Services Studio – it will be used for the EVPN over the Enterprise Core Network. This will avoid the limitation of a vlan id cannot be reused even if it is on a different network (vlan between border leafs and edge router for example)

## Slide 27
Example3: L3EVPN on Enterprise Core

## Slide 28: Example3 Tags
See tagsfile.txt to load tags through the API with tagman.py
DC-Pod:1 - EOS14
DC-Pod:1 - EOS6
DC-Pod:1 - EOS8
DC-Pod:2 - EOS3
DC-Pod:2 - EOS4
DC-Pod:2 - EOS9
DC:DC-eos3-eos4-eos9 - EOS3
DC:DC-eos3-eos4-eos9 - EOS4
DC:DC-eos3-eos4-eos9 - EOS9
DC:DC-eos6-eos8-eos14 - EOS14
DC:DC-eos6-eos8-eos14 - EOS6
DC:DC-eos6-eos8-eos14 - EOS8
Edge-Router-Domain:1 - EOS1
Edge-Router-Domain:18 - EOS18
Edge-Router-Domain:20 - EOS20
Edge-Router-Domain:4 - EOS4
Edge-Router-Domain:5 - EOS5
Edge-Router-Domain:6 - EOS6
Leaf-Domain:1 - EOS6
Leaf-Domain:2 - EOS8
Leaf-Domain:3 - EOS3
Leaf-Domain:4 - EOS4
Leaf-Number:1 - EOS4
Leaf-Number:1 - EOS6
Leaf-Number:2 - EOS3
Leaf-Number:2 - EOS8
Network:CoreNet-eos1-eos2-eos5-eos17 - EOS1
Network:CoreNet-eos1-eos2-eos5-eos17 - EOS17
Network:CoreNet-eos1-eos2-eos5-eos17 - EOS2
Network:CoreNet-eos1-eos2-eos5-eos17 - EOS5
Network:DC-Border-Leaf-eos4 - EOS4
Network:DC-Border-Leaf-eos6 - EOS6
Network:DC-End-device-eos18 - EOS18
Network:DC-End-device-eos20 - EOS20
Role:Core - EOS2
Role:Edge-Router - EOS1
Role:Edge-Router - EOS5
Role:Leaf - EOS3
Role:Leaf - EOS4
Role:Leaf - EOS6
Role:Leaf - EOS8
Role:RR - EOS17
Role:Spine - EOS14
Role:Spine - EOS9
Spine-Number:1 - EOS14
Spine-Number:1 - EOS9
router_bgp.router_id:1.1.1.1 - EOS1
router_bgp.router_id:17.17.17.17
router_bgp.router_id:2.2.2.2 - EOS2
router_bgp.router_id:5.5.5.5 - EOS5

## Slide 29: Device Selection
Clone the EVPN Services Studio. This clone will be used for the EVPN over the Enterprise Core Network

## Slide 30: Test
From eos18 ping eos20 14.14.14.2
You may have to clear the arp cache on eos18 between the mac address of its default gateway has changed from the previous example

## Slide 31: Example 4 Routing Campus to ISP, OSPF & eBGP

## Slide 32: Example4: Routing OSPF Campus and eBGP to ISP Campus receives Default Route Campus edge router has full Internet routes
In this example the Enterprise Routing Studio, consisting of 3 Edge Routers route a Campus to the Internet
ISP sends full routes but Edge Router sends only a default route to the Campus Splines
Ping from Campus switch eos12 15.15.15.4/24 to eos10 on ISP network 10.10.10.10

## Slide 33
Example4:
edge
core

## Slide 34: Example 4 Tags
See tagsfile.txt to load tags through the API with tagman.py
Campus-Pod:12 - EOS12
Campus:Campus-eos11-eos12-eos13 - EOS11
Campus:Campus-eos11-eos12-eos13 - EOS12
Campus:Campus-eos11-eos12-eos13 - EOS13
Edge-Router-Domain:7 - EOS7
Edge-Router-Domain:Campus11-13 - EOS11
Edge-Router-Domain:Campus11-13 - EOS13
Network:CoreNet-eos1-eos2-eos5-eos11-eos13 - EOS1
Network:CoreNet-eos1-eos2-eos5-eos11-eos13 - EOS11
Network:CoreNet-eos1-eos2-eos5-eos11-eos13 - EOS13
Network:CoreNet-eos1-eos2-eos5-eos11-eos13 - EOS2
Network:CoreNet-eos1-eos2-eos5-eos11-eos13 - EOS5
Network:ISP-eos7-eos10-eos19 - EOS10
Network:ISP-eos7-eos10-eos19 - EOS19
Network:ISP-eos7-eos10-eos19 - EOS7
Role:Core - EOS1
Role:Core - EOS10
Role:Core - EOS19
Role:Edge-Router - EOS11
Role:Edge-Router - EOS13
Role:Edge-Router - EOS2
Role:Edge-Router - EOS5
Role:Edge-Router - EOS7
router_bgp.router_id:1.1.1.1 - EOS1
router_bgp.router_id:10.10.10.10 - EOS10
router_bgp.router_id:11.11.11.11 - EOS11
router_bgp.router_id:13.13.13.13 - EOS13
router_bgp.router_id:19.19.19.19 - EOS19
router_bgp.router_id:7.7.7.7 - EOS7

## Slide 35: Device Selection

## Slide 36: Test
From Campus switch eos12 ping to eos10 on the ISP network 10.10.10.10

## Slide 37: Example 5 Routing Campus to Campus + EVPN

## Slide 38: Example5: Routing OSPF Campus to Campus + L2 vlan stretch between Campus
In this example the Enterprise Routing Studio, consisting of 3 Edge Routers route a Campus to the Internet
ISP sends full routes but Edge Router sends only a default route to the Campus Splines
Ping from Campus switch eos12 15.15.15.4/24 to eos10 on ISP network 10.10.10.10

## Slide 39
Example5: Routing Campus to Campus + EVPN

## Slide 40: Example 5 Tags
See tagsfile.txt to load tags through the API with tagman.py
Campus-Pod:12 - EOS12
Campus-Pod:3 - EOS3
Campus-Pod:4 - EOS4
Campus:Campus-eos11-eos12-eos13 - EOS11
Campus:Campus-eos11-eos12-eos13 - EOS12
Campus:Campus-eos11-eos12-eos13 - EOS13
Campus:Campus-eos2-eos3-eos4-eos5 - EOS2
Campus:Campus-eos2-eos3-eos4-eos5 - EOS3
Campus:Campus-eos2-eos3-eos4-eos5 - EOS4
Campus:Campus-eos2-eos3-eos4-eos5 - EOS5
Edge-Router-Domain:20 - EOS20
Edge-Router-Domain:7 - EOS7
Edge-Router-Domain:9 - EOS9
Edge-Router-Domain:Campus11-13 - EOS11
Edge-Router-Domain:Campus11-13 - EOS13
Edge-Router-Domain:Campus2-5 - EOS2
Edge-Router-Domain:Campus2-5 - EOS5
Network:Campus-EndDevice-eos20 - EOS20
Network:Campus-EndDevice-eos9 - EOS9
Network:CoreNet-eos1-eos2-eos5-eos11-eos13-eos17 - EOS1
Network:CoreNet-eos1-eos2-eos5-eos11-eos13-eos17 - EOS11
Network:CoreNet-eos1-eos2-eos5-eos11-eos13-eos17 - EOS13
Network:CoreNet-eos1-eos2-eos5-eos11-eos13-eos17 - EOS17
Network:CoreNet-eos1-eos2-eos5-eos11-eos13-eos17 - EOS2
Network:CoreNet-eos1-eos2-eos5-eos11-eos13-eos17 - EOS5
Network:ISP-eos7-eos10-eos19 - EOS10
Network:ISP-eos7-eos10-eos19 - EOS19
Network:ISP-eos7-eos10-eos19 - EOS7
Role:Core - EOS1
Role:Core - EOS10
Role:Core - EOS19
Role:Edge-Router - EOS11
Role:Edge-Router - EOS13
Role:Edge-Router - EOS2
Role:Edge-Router - EOS20
Role:Edge-Router - EOS5
Role:Edge-Router - EOS7
Role:RR - EOS17
router_bgp.router_id:1.1.1.1 - EOS1
router_bgp.router_id:10.10.10.10 - EOS10
router_bgp.router_id:11.11.11.11 - EOS11
router_bgp.router_id:13.13.13.13 - EOS13
router_bgp.router_id:17.17.17.17 - EOS17
router_bgp.router_id:19.19.19.19 - EOS19
router_bgp.router_id:2.2.2.2 - EOS2
router_bgp.router_id:5.5.5.5 - EOS5
router_bgp.router_id:7.7.7.7 - EOS7

## Slide 41: Device Selection

## Slide 42: Test
From Campus switch eos12 ping DC end device eos9 15.15.15.2
From Campus switch eos12 ping to eos10 on the ISP network 10.10.10.10
From DC end device ping eos10 on ISP network 10.10.10.10

## Slide 43: Example 6 Border Leaf OSPF to Enterprise Core

## Slide 44: Example6: Border Leaf OSPF to Enterprise Core L3 DC has no overlay and runs OSPF on Border Leafs
In this example the Enterprise Routing Studio, consisting of 4 Edge Routers and 2 Core Routers routes a L3DC using L3LS Studio to an L2 DC using the Campus Studio.
On the border leafs on the L3 DC BGP to OSPF redistribution is configured using the Enterprise Routing Studio
Border Leafs are set to the same ASN in the L3LS Studio to prevent routing loops

## Slide 45
Example6:

## Slide 46: Example 6 Tags
See tagsfile.txt to load tags through the API with tagman.py
Campus-Pod:L2DC-eos12 - EOS12
Campus:L2DC-eos11-eos12-eos13 - EOS11
Campus:L2DC-eos11-eos12-eos13 - EOS12
Campus:L2DC-eos11-eos12-eos13 - EOS13
Campus:L3DC-End-device-eos9 - EOS9
DC-Pod:1 - EOS2
DC-Pod:1 - EOS3
DC-Pod:1 - EOS4
DC-Pod:1 - EOS5
DC-Pod:1 - EOS9
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS2
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS3
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS4
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS5
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS9
Edge-Router-Domain:11-13 - EOS11
Edge-Router-Domain:11-13 - EOS13
Edge-Router-Domain:2 - EOS2
Edge-Router-Domain:5 - EOS5
Edge-Router-Domain:9 - EOS9
Leaf-Domain:2 - EOS2
Leaf-Domain:5 - EOS5
Leaf-Domain:9 - EOS9
Leaf-Number:1 - EOS2
Leaf-Number:2 - EOS5
Leaf-Number:3 - EOS9
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS1
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS11
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS13
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS2
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS5
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS6
Network:L3DC-End-device-eos9 - EOS9
Role:Core - EOS1
Role:Core - EOS6
Role:Edge-Router - EOS11
Role:Edge-Router - EOS13
Role:Edge-Router - EOS2
Role:Edge-Router - EOS5
Role:Leaf - EOS2
Role:Leaf - EOS5
Role:Leaf - EOS9
Role:Spine - EOS3
Role:Spine - EOS4
Spine-Number:1 - EOS4
Spine-Number:2 - EOS3
router_bgp.router_id:1.1.1.1 - EOS1
router_bgp.router_id:11.11.11.11 - EOS11
router_bgp.router_id:13.13.13.13 - EOS13
router_bgp.router_id:6.6.6.6 - EOS6

## Slide 47: Device Selection

## Slide 48: Test
From Campus switch eos12 ping DC Leaf eos9 14.14.14.2
From DC Leaf eos9 14.14.14.2 ping Campus switch eos12

## Slide 49: Example 7 OSPF per VRF Border Leaf

## Slide 50: Example7: OSPF per Border Leaf VRF L3 DC has EVPN overlay and runs OSPF on Border Leafs in VRF
In this example the Enterprise Routing Studio, consisting of 4 Edge Routers and 2 Core Routers routes a L3DC using L3LS Studio to an L2 DC using the Campus Studio.
On the border leafs on the L3 DC BGP to OSPF redistribution is configured using the Enterprise Routing Studio
Border Leafs are set to the same ASN in the L3LS Studio to prevent routing loops

## Slide 51
Example7:

## Slide 52: Example 7 Tags
See tagsfile.txt to load tags through the API with tagman.py
Campus-Pod:L2DC-eos12 - EOS12
Campus:L2DC-eos11-eos12-eos13 - EOS11
Campus:L2DC-eos11-eos12-eos13 - EOS12
Campus:L2DC-eos11-eos12-eos13 - EOS13
Campus:L3DC-End-device-eos9 - EOS9
DC-Pod:1 - EOS2
DC-Pod:1 - EOS3
DC-Pod:1 - EOS4
DC-Pod:1 - EOS5
DC-Pod:1 - EOS9
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS2
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS3
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS4
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS5
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS9
Edge-Router-Domain:11-13 - EOS11
Edge-Router-Domain:11-13 - EOS13
Edge-Router-Domain:2 - EOS2
Edge-Router-Domain:5 - EOS5
Edge-Router-Domain:9 - EOS9
Leaf-Domain:2 - EOS2
Leaf-Domain:5 - EOS5
Leaf-Domain:9 - EOS9
Leaf-Number:1 - EOS2
Leaf-Number:2 - EOS5
Leaf-Number:3 - EOS9
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS1
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS11
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS13
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS2
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS5
Network:CoreNet-eos1-eos2-eos5-eos6-eos11-eos13 - EOS6
Network:L3DC-End-device-eos9 - EOS9
Role:Core - EOS1
Role:Core - EOS6
Role:Edge-Router - EOS11
Role:Edge-Router - EOS13
Role:Edge-Router - EOS2
Role:Edge-Router - EOS5
Role:Leaf - EOS2
Role:Leaf - EOS5
Role:Leaf - EOS9
Role:Spine - EOS3
Role:Spine - EOS4
Spine-Number:1 - EOS4
Spine-Number:2 - EOS3
router_bgp.router_id:1.1.1.1 - EOS1
router_bgp.router_id:11.11.11.11 - EOS11
router_bgp.router_id:13.13.13.13 - EOS13
router_bgp.router_id:6.6.6.6 - EOS6

## Slide 53: Device Selection

## Slide 54: Test
From Campus switch eos12 ping DC Leaf eos9 14.14.14.2
From DC Leaf eos9 14.14.14.2 ping Campus switch eos12

## Slide 55: Example 8 BGP Enterprise Core Non-Overlay DC

## Slide 56: Example8: BGP Enterprise Core eBGP to Border Leafs, Overlay enabled DC
In this example the Enterprise Routing Studio, consisting of 2 Edge Routers in a Camus, 2 Core Routers and 2 Edge Routers in L3DC

## Slide 57
Example8:

## Slide 58: Example 8 Tags
See tagsfile.txt to load tags through the API with tagman.py
Campus-Pod:12 - EOS12
Campus:L2DC-eos11-eos12-eos13 - EOS11
Campus:L2DC-eos11-eos12-eos13 - EOS12
Campus:L2DC-eos11-eos12-eos13 - EOS13
Campus:L3DC-End-device-eos9 - EOS9
DC-Pod:1 - EOS2
DC-Pod:1 - EOS3
DC-Pod:1 - EOS4
DC-Pod:1 - EOS5
DC-Pod:1 - EOS9
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS2
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS3
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS4
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS5
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS9
Edge-Router-Domain:11-13 - EOS11
Edge-Router-Domain:11-13 - EOS13
Edge-Router-Domain:2 - EOS2
Edge-Router-Domain:5 - EOS5
Edge-Router-Domain:9 - EOS9
Leaf-Domain:2 - EOS2
Leaf-Domain:5 - EOS5
Leaf-Domain:9 - EOS9
Leaf-Number:1 - EOS2
Leaf-Number:2 - EOS5
Leaf-Number:3 - EOS9
Network:CoreNet-eos1-eos6 - EOS1
Network:CoreNet-eos1-eos6 - EOS6
Network:L2DC-eos11-eos13 - EOS11
Network:L2DC-eos11-eos13 - EOS13
Network:L3DC-Border-Leafs-eos2-eos5 - EOS2
Network:L3DC-Border-Leafs-eos2-eos5 - EOS5
Network:L3DC-End-device-eos9 - EOS9
Role:Core - EOS1
Role:Core - EOS6
Role:Edge-Router - EOS11
Role:Edge-Router - EOS13
Role:Edge-Router - EOS2
Role:Edge-Router - EOS5
Role:Leaf - EOS2
Role:Leaf - EOS5
Role:Leaf - EOS9
Role:Spine - EOS3
Role:Spine - EOS4
Spine-Number:1 - EOS3
Spine-Number:2 - EOS4
router_bgp.router_id:1.1.1.1 - EOS1
router_bgp.router_id:11.11.11.11 - EOS11
router_bgp.router_id:13.13.13.13 - EOS13
router_bgp.router_id:6.6.6.6 - EOS6

## Slide 59: Device Selection

## Slide 60: Test
From Campus switch eos12 ping DC Leaf eos9 14.14.14.2
From DC Leaf eos9 14.14.14.2 ping Campus switch eos12

## Slide 61: Example 9 VRF Lite, Overlay DC

## Slide 62: Example9: VRF Lite Core and DC w Overlay L3DC EVPN/VXLAN Overlay enabled
In this example the Enterprise Routing Studio, consisting of 2 Edge Routers in a Camus, 2 Core Routers and 2 Edge Routers in L3DC

## Slide 63
Example9:

## Slide 64: Example 9 Tags
See tagsfile.txt to load tags through the API with tagman.py
Campus-Pod:L2DC-eos12 - EOS12
Campus:L2DC-eos11-eos12-eos13 - EOS11
Campus:L2DC-eos11-eos12-eos13 - EOS12
Campus:L2DC-eos11-eos12-eos13 - EOS13
Campus:L3DC-End-device-eos9 - EOS9
DC-Pod:1 - EOS2
DC-Pod:1 - EOS3
DC-Pod:1 - EOS4
DC-Pod:1 - EOS5
DC-Pod:1 - EOS9
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS2
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS3
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS4
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS5
DC:L3DC-eos2-eos3-eos4-eos5-eos9 - EOS9
Edge-Router-Domain:11-13 - EOS11
Edge-Router-Domain:11-13 - EOS13
Edge-Router-Domain:2 - EOS2
Edge-Router-Domain:5 - EOS5
Edge-Router-Domain:9 - EOS9
Leaf-Domain:2 - EOS2
Leaf-Domain:5 - EOS5
Leaf-Domain:9 - EOS9
Leaf-Number:1 - EOS2
Leaf-Number:2 - EOS5
Leaf-Number:3 - EOS9
Network:CoreNet-eos1-eos6 - EOS1
Network:CoreNet-eos1-eos6 - EOS6
Network:L2DC-eos11-eos13 - EOS11
Network:L2DC-eos11-eos13 - EOS13
Network:L3DC-Border-Leafs-eos2-eos5 - EOS2
Network:L3DC-Border-Leafs-eos2-eos5 - EOS5
Network:L3DC-End-device-eos9 - EOS9
Role:Core - EOS1
Role:Core - EOS6
Role:Edge-Router - EOS11
Role:Edge-Router - EOS13
Role:Edge-Router - EOS2
Role:Edge-Router - EOS5
Role:Leaf - EOS2
Role:Leaf - EOS5
Role:Leaf - EOS9
Role:Spine - EOS3
Role:Spine - EOS4
Spine-Number:1 - EOS3
Spine-Number:2 - EOS4
router_bgp.router_id:1.1.1.1 - EOS1
router_bgp.router_id:11.11.11.11 - EOS11
router_bgp.router_id:13.13.13.13 - EOS13
router_bgp.router_id:6.6.6.6 - EOS6

## Slide 65: Device Selection

## Slide 66: Test
From Campus switch eos12 ping DC Leaf eos9 14.14.14.2