## Slide 1: Studios Interop
For ATD Advanced Routing Environment
Brian Hayes

## Slide 2: Overview
Enterprise Routing
EVPN Services
L3LS
Campus
Interface Configuration
Studios Used
These slides contain examples and instructions of how to build end to end topologies with services in Cloud Vision Studios. Featured is the Enterprise Routing Studio that is used to inter-connect Campus and DCs together.
Arista Avanced Routing ATDs are used for these examples because they supply an easy environment for getting familiar with the interop between Studios that is required to configure complete networks.
Topologies Covered
DCI
Campus Interconnect
ISP Connections
EVPN for Enterprise

## Slide 3: Complete Topology of the ATD
These examples use a sub-set of this topology for each Interconnect example

## Slide 4: Launch the Advanced Routing ATD
https://testdrive.arista.com/ and launch the latest version of CloudVision

## Slide 5: To import and export Studios Inputs files This is an Alpha feature and needs to be enabled in CV settings. This allows the example files that go with these slides to be uploaded.

## Slide 6: CV Studios GitHub site Clone these files to your laptop – details on next slide

## Slide 7: Inputs Files
Clone the repository here:
https://github.com/arista-netdevops-community/CloudVisionPortal-Examples
git clone https://github.com/arista-netdevops-community/CloudVisionPortal-Examples.git
Enterprise Routing Studio is also found in this repository and must be loaded to the ATD until it is a built-in in the CV version in the ATD (Kent)
Files found here:
https://github.com/arista-netdevops-community/CloudVisionPortal-Examples/tree/master/CloudVision_Studios/Enterprise%20Routing%20Studio%20Examples
Input data and tags have been put into files to upload into CV

## Slide 8: Import Enterprise Routing Studio into ATD
Once Kent version of CV is released this step is not needed because the Enterprise Routing will be a "Built-In Studio".
File location:
https://github.com/arista-netdevops-community/CloudVisionPortal-Examples/tree/master/CloudVision_Studios/Enterprise%20Routing

## Slide 9: Import to CV the Inputs for each example
All Files found here:
https://github.com/arista-netdevops-community/CloudVisionPortal-Examples/tree/master/CloudVision_Studios/Enterprise%20Routing%20Studio%20Examples
Note: The interface configuration built-in studio has a bug, please use the fixed version found in the above repository

## Slide 10: Note: Some Tags are created automatically by Studios and do not need to be entered
L3LS Studio and Enterprise Routing Studio will set ASN tags. The user does not need to create them.
L3LS Studio will set these lo0/router ID Tags. The user must create them in the Enterprise Routing Studio if using ISIS or EVPN.

## Slide 11: Other Notes
Be sure to accept "updates" in the Inventory and Topology Studio prior to Selecting devices in each Studio
Be sure to check that the drop down yes/no fields in EVPN Services and Interface Studio are populated by the inputs files – Jackson release had a problem with this
When changing between examples be sure to clear the arp cache in the end devices prior to sending a ping – the mac of the gw may have changed
Use the version of Interface Studio on the github site – it fixes a bug where when changing from a routed port to bridged port is missing the "switchport" command
Use the version of the EVPN Services Studio in the github site – it has the added capability of redistributing OSPF into VRFs it creates
Both the router_bgp.as Tag and the router_bgp.router_id Tag (for lo0) are written by the L3LS Studio and do not have to be entered by the user but if Enterprise Routing Studio has EVPN/VXLAN enabled the router_bgp.router_id (lo0) tag must be added. These tags are in the tagsfile.txt
Using multiple role tags is only available in CV version Kent and beyond. If using Jackson do not use the Role: Edge-Router tag if L3LS is also using Role tags.

## Slide 12: If doing an upgrade of CV, new Studios are in a workspace when the upgrade completes Submit this workspace! To add any new Studios permanently

## Slide 13: Uploading Tags files with tagman.py
Tagman.py is a script written by Engineering to make saving and creating tag more easy. The tags are exported as a txt file and can then be re-imported or deleted.
See next slide for setting up your laptop to run tagman.py
The tagsfile defaults to using hostname but there is also an option for using serial number.
Use the –help option for the required syntax.
Example:
python tagman.py -u arista -p aristaf613 -c unf-arista-campus-vlab-1-11f86e35.topo.testdrive.arista.com -f tagsfile.txt -a export

## Slide 14: Tagman.py setup

## Slide 15: Interface Configuration Studio setup
Create a profile called Trunk in the Interface Configuration Studio. It will be reused throughout the examples.

## Slide 16: Interface Configuration Studio setup
End devices plugged into edge switches use vlan tagging so the edge ports are configured as trunks. The ports requiring this profile are given for each example.

## Slide 17: Example1 DC Gateway Router

## Slide 18: Example1 DC Gateway Router This example also routes between DCs with OSPF
In this example the Enterprise Routing Studio, consisting of a Core Router and 2 Edge Routers, connects 2 DC together
The DC border leafs have a trunk port to Edge Router and another leaf has a trunk to the end device
A vlan in 1 DC containing the end device is routed to a different vlan in another DC
Each vlan is a L2 EVPN in Each DC with the end device and the Edge Router in the VPN.
The Edge Router is the default gw for end devices in each DC. (A switch is used for the end device to launch pings from)
Example2 and example3 build on example 1

## Slide 19: Example1 Detail

## Slide 20: Example1 Tags
DC, DC-eos3-eos4-eos9, eos3
DC, DC-eos3-eos4-eos9, eos4
DC, DC-eos3-eos4-eos9, eos9
DC, DC-eos6-eos8-eos14, eos14
DC, DC-eos6-eos8-eos14, eos6
DC, DC-eos6-eos8-eos14, eos8
DC-Pod, 1, eos14
DC-Pod, 1, eos6
DC-Pod, 1, eos8
DC-Pod, 2, eos3
DC-Pod, 2, eos4
DC-Pod, 2, eos9
Edge-Router-Domain, 1, eos1
Edge-Router-Domain, 18, eos18
Edge-Router-Domain, 20, eos20
Edge-Router-Domain, 5, eos5
Leaf-Domain, 1, eos6
Leaf-Domain, 2, eos8
Leaf-Domain, 3, eos3
Leaf-Domain, 4, eos4
Leaf-Number, 1, eos4
Leaf-Number, 1, eos6
Leaf-Number, 2, eos3
Leaf-Number, 2, eos8
Network, DC-End-device-eos18, eos18
Network, DC-End-device-eos20, eos20
Network, Ex1-CoreNet-eos1-eos2-eos5, eos1
Network, Ex1-CoreNet-eos1-eos2-eos5, eos2
Network, Ex1-CoreNet-eos1-eos2-eos5, eos5
Role, Core, eos2
Role, Edge-Router, eos1
Role, Edge-Router, eos5
Role, Leaf, eos3
Role, Leaf, eos4
Role, Leaf, eos6
Role, Leaf, eos8
Role, Spine, eos14
Role, Spine, eos9
Spine-Number, 1, eos14
Spine-Number, 1, eos9
router_bgp.as, 65000, eos14
router_bgp.as, 65001, eos6
router_bgp.as, 65002, eos8
router_bgp.as, 65010, eos9
router_bgp.as, 65013, eos3
router_bgp.as, 65014, eos4
router_bgp.as, 7, eos1
router_bgp.as, 7, eos2
router_bgp.as, 7, eos5
router_bgp.router_id, 1.1.1.1, eos1
router_bgp.router_id, 172.16.0.1, eos14
router_bgp.router_id, 172.16.0.1, eos9
router_bgp.router_id, 172.16.0.2, eos4
router_bgp.router_id, 172.16.0.2, eos6
router_bgp.router_id, 172.16.0.3, eos3
router_bgp.router_id, 172.16.0.3, eos8
router_bgp.router_id, 2.2.2.2, eos2
router_bgp.router_id, 5.5.5.5, eos5

## Slide 21: Example1 Device Selection
Enterprise Routing Studio
L3LS Studio
EVPN Studio
Interfaces Studio

## Slide 22: Example1 Interface Studio Ports
Interfaces Studio
Ethernet 6
Ethernet 3
Ethernet 4
Ethernet 5
Apply “Trunk” profile to these ports. See slide 15

## Slide 23: Example1 Traffic Test
From eos18 ping to eos20 14.14.14.2

## Slide 24: Example2 BGP DC Interconnect

## Slide 25: Example2 BGP DC Interconnect DCs route to each other in this example
In this example the Enterprise Routing Studio, consisting of a Core Router and 2 Edge Routers, connects 2 DC together
The DC border leafs have a trunk port to Edge Router and another leaf has a trunk to the end device
A vlan in 1 DC containing the end device is routed to a different vlan in another DC
Each vlan is a L3 EVPN in Each DC with the end device and the Edge Router in the VPN.
The Edge Router is the default gw for end devices in each DC. (A switch is used for the end device to ping from)
Ping from eos18 13.13.13.2/24 to eos 20 14.14.14.2/24

## Slide 26: Example2 Detail

## Slide 27: Example2 Tags
DC, DC-eos3-eos4-eos9, eos3
DC, DC-eos3-eos4-eos9, eos4
DC, DC-eos3-eos4-eos9, eos9
DC, DC-eos6-eos8-eos14, eos14
DC, DC-eos6-eos8-eos14, eos6
DC, DC-eos6-eos8-eos14, eos8
DC-Pod, 1, eos14
DC-Pod, 1, eos6
DC-Pod, 1, eos8
DC-Pod, 2, eos3
DC-Pod, 2, eos4
DC-Pod, 2, eos9
Edge-Router-Domain, 1, eos1
Edge-Router-Domain, 18, eos18
Edge-Router-Domain, 20, eos20
Edge-Router-Domain, 4, eos4
Edge-Router-Domain, 5, eos5
Edge-Router-Domain, 6, eos6
Leaf-Domain, 1, eos6
Leaf-Domain, 2, eos8
Leaf-Domain, 3, eos3
Leaf-Domain, 4, eos4
Leaf-Number, 1, eos4
Leaf-Number, 1, eos6
Leaf-Number, 2, eos3
Leaf-Number, 2, eos8
Network, DC-Border-Leaf-eos4, eos4
Network, DC-Border-Leaf-eos6, eos6
Network, DC-End-device-eos18, eos18
Network, DC-End-device-eos20, eos20
Network, Ex2-CoreNet-eos1-eos2-eos5, eos1
Network, Ex2-CoreNet-eos1-eos2-eos5, eos2
Network, Ex2-CoreNet-eos1-eos2-eos5, eos5
Role, Core, eos2
Role, Edge-Router, eos1
Role, Edge-Router, eos5
Role, Leaf, eos3
Role, Leaf, eos4
Role, Leaf, eos6
Role, Leaf, eos8
Role, Spine, eos14
Role, Spine, eos9
Spine-Number, 1, eos14
Spine-Number, 1, eos9
router_bgp.as, 65000, eos14
router_bgp.as, 65001, eos6
router_bgp.as, 65002, eos8
router_bgp.as, 65010, eos9
router_bgp.as, 65013, eos3
router_bgp.as, 65014, eos4
router_bgp.as, 7, eos1
router_bgp.as, 7, eos2
router_bgp.as, 7, eos5
router_bgp.router_id, 1.1.1.1, eos1
router_bgp.router_id, 172.16.0.1, eos14
router_bgp.router_id, 172.16.0.1, eos9
router_bgp.router_id, 172.16.0.2, eos4
router_bgp.router_id, 172.16.0.2, eos6
router_bgp.router_id, 172.16.0.3, eos3
router_bgp.router_id, 172.16.0.3, eos8
router_bgp.router_id, 2.2.2.2, eos2
router_bgp.router_id, 5.5.5.5, eos5

## Slide 28: Example2 Device Selection
Enterprise Routing Studio
L3LS Studio
EVPN Studio
Interfaces Studio

## Slide 29: Example1 Interface Studio Ports
Interfaces Studio
Ethernet 6
Ethernet 5
Apply “Trunk” profile to these ports. See slide 15

## Slide 30: Example2 Traffic Test
From eos18 ping eos20 14.14.14.2
You may have to clear the arp cache on eos18 between the mac address of its default gateway has changed from the previous example

## Slide 31: Example3 Campus to ISP

## Slide 32: Example3 Campus to ISP BGP and OSPF default route
In this example the Enterprise Routing Studio, consisting of 2 Edge Routers and a Core Router connects Campus to the Internet
ISP sends full routes to border router but only a default route is send into the Enterprise network
MLAG is configured in the Campus Studio and Enterprise Routing Studio so an OSPF adjacency is formed over the MLAG peer link.

## Slide 33
Example3 Detail
edge
core

## Slide 34: Example3 Tags
Campus, Campus-eos11-eos12-eos13, eos11
Campus, Campus-eos11-eos12-eos13, eos12
Campus, Campus-eos11-eos12-eos13, eos13
Campus-Pod, 12, eos12
Edge-Router-Domain, 7, eos7
Edge-Router-Domain, Campus11-13, eos11
Edge-Router-Domain, Campus11-13, eos13
Network, Ex3-CoreNet-eos1-eos11-eos13, eos1
Network, Ex3-CoreNet-eos1-eos11-eos13, eos11
Network, Ex3-CoreNet-eos1-eos11-eos13, eos13
Network, ISP-eos7-eos10-eos19, eos10
Network, ISP-eos7-eos10-eos19, eos19
Network, ISP-eos7-eos10-eos19, eos7
Role, Core, eos1
Role, Core, eos10
Role, Core, eos19
Role, Edge-Router, eos11
Role, Edge-Router, eos13
Role, Edge-Router, eos7
router_bgp.as, 7, eos1
router_bgp.as, 7, eos11
router_bgp.as, 7, eos13
router_bgp.as, 8, eos10
router_bgp.as, 8, eos19
router_bgp.as, 8, eos7
router_bgp.router_id, 1.1.1.1, eos1
router_bgp.router_id, 10.10.10.10, eos10
router_bgp.router_id, 11.11.11.11, eos11
router_bgp.router_id, 13.13.13.13, eos13
router_bgp.router_id, 19.19.19.19, eos19
router_bgp.router_id, 7.7.7.7, eos7

## Slide 35: Example3 Device Selection
Enterprise Routing Studio
Campus Studio

## Slide 36: Example 3 Traffic Test
From Campus switch eos12 ping to eos10 on the ISP network 10.10.10.10

## Slide 37: Example4 Campus to Campus EVPN

## Slide 38: Example4 Campus to Campus EVPN L2 stretch over the routed Core network
In this example the Enterprise Routing Studio, consisting of 4 Edge Routers and 1 Core Router route a Campus to the Internet
ISP sends full routes but Edge Router sends only a default route to the Campus Splines
Ping from Campus switch eos12 15.15.15.4/24 to eos10 on ISP network 10.10.10.10

## Slide 39
Example4 Detail

## Slide 40: Example4 Tags
Campus, Campus-eos11-eos12-eos13, eos11
Campus, Campus-eos11-eos12-eos13, eos12
Campus, Campus-eos11-eos12-eos13, eos13
Campus, Campus-eos2-eos3-eos4-eos5, eos2
Campus, Campus-eos2-eos3-eos4-eos5, eos3
Campus, Campus-eos2-eos3-eos4-eos5, eos4
Campus, Campus-eos2-eos3-eos4-eos5, eos5
Campus-Pod, 12, eos12
Campus-Pod, 3, eos3
Campus-Pod, 4, eos4
Edge-Router-Domain, 20, eos20
Edge-Router-Domain, 7, eos7
Edge-Router-Domain, 9, eos9
Edge-Router-Domain, Campus11-13, eos11
Edge-Router-Domain, Campus11-13, eos13
Edge-Router-Domain, Campus2-5, eos2
Edge-Router-Domain, Campus2-5, eos5
Network, Campus-EndDevice-eos20, eos20
Network, Campus-EndDevice-eos9, eos9
Network, Ex4-CoreNet-eos1-eos2-eos5-eos11-eos13-eos17, eos1
Network, Ex4-CoreNet-eos1-eos2-eos5-eos11-eos13-eos17, eos11
Network, Ex4-CoreNet-eos1-eos2-eos5-eos11-eos13-eos17, eos13
Network, Ex4-CoreNet-eos1-eos2-eos5-eos11-eos13-eos17, eos17
Network, Ex4-CoreNet-eos1-eos2-eos5-eos11-eos13-eos17, eos2
Network, Ex4-CoreNet-eos1-eos2-eos5-eos11-eos13-eos17, eos5
Network, ISP-eos7-eos10-eos19, eos10
Network, ISP-eos7-eos10-eos19, eos19
Network, ISP-eos7-eos10-eos19, eos7
Role, Core, eos1
Role, Core, eos10
Role, Core, eos19
Role, Edge-Router, eos11
Role, Edge-Router, eos13
Role, Edge-Router, eos2
Role, Edge-Router, eos20
Role, Edge-Router, eos5
Role, Edge-Router, eos7
Role, RR, eos17
router_bgp.as, 7, eos1
router_bgp.as, 7, eos11
router_bgp.as, 7, eos13
router_bgp.as, 7, eos17
router_bgp.as, 7, eos2
router_bgp.as, 7, eos5
router_bgp.as, 8, eos10
router_bgp.as, 8, eos19
router_bgp.as, 8, eos7
router_bgp.router_id, 1.1.1.1, eos1
router_bgp.router_id, 10.10.10.10, eos10
router_bgp.router_id, 11.11.11.11, eos11
router_bgp.router_id, 13.13.13.13, eos13
router_bgp.router_id, 17.17.17.17, eos17
router_bgp.router_id, 19.19.19.19, eos19
router_bgp.router_id, 2.2.2.2, eos2
router_bgp.router_id, 5.5.5.5, eos5
router_bgp.router_id, 7.7.7.7, eos7

## Slide 41: Example4 Device Selection
Enterprise Routing Studio
Campus Studio
EVPN Studio
Interface Configuration Studio

## Slide 42: Example4 Interface Studio Ports
Interfaces Studio
Ethernet 1
Ethernet 6
Apply “Trunk” profile to these ports. See slide 15

## Slide 43: Example4 Traffic Test
From Campus switch eos12 ping DC end device eos9 15.15.15.133 and eos20 15.15.15.134
From Campus switches eos12, ping to eos10 10.10.10.10 and eos19 19.19.19.19 on the ISP Network
From Campus end devices eos9 and eos20, ping to eos10 10.10.10.10 and eos19 19.19.19.19 on the ISP Network

## Slide 44: Example5 Campus BGP Underlay

## Slide 45: Example5 Campus BGP Underlay L2 stretch over the routed Core network
In this example the Enterprise Routing Studio, consisting of 4 Edge Routers and a Core Router route a Campus to the Internet
ISP sends default route
Ping from Campus switch eos12 15.15.15.4/24 to eos10 on ISP network 10.10.10.10
Note: This example uses “Core Router can also be a RR” feature that came out post Kent

## Slide 46: Example5 Detail

## Slide 47: Example5 Tags
Campus, Campus-eos11-eos12-eos13, eos11
Campus, Campus-eos11-eos12-eos13, eos12
Campus, Campus-eos11-eos12-eos13, eos13
Campus, Campus-eos2-eos3-eos4-eos5, eos2
Campus, Campus-eos2-eos3-eos4-eos5, eos3
Campus, Campus-eos2-eos3-eos4-eos5, eos4
Campus, Campus-eos2-eos3-eos4-eos5, eos5
Campus-Pod, 12, eos12
Campus-Pod, 3, eos3
Campus-Pod, 4, eos4
Edge-Router-Domain, 20, eos20
Edge-Router-Domain, 7, eos7
Edge-Router-Domain, 9, eos9
Edge-Router-Domain, Campus11-13, eos11
Edge-Router-Domain, Campus11-13, eos13
Edge-Router-Domain, Campus2-5, eos2
Edge-Router-Domain, Campus2-5, eos5
Network, Campus-EndDevice-eos20, eos20
Network, Campus-EndDevice-eos9, eos9
Network, Ex5-CoreNet-eos1-eos2-eos5-eos11-eos13, eos1
Network, Ex5-CoreNet-eos1-eos2-eos5-eos11-eos13, eos11
Network, Ex5-CoreNet-eos1-eos2-eos5-eos11-eos13, eos13
Network, Ex5-CoreNet-eos1-eos2-eos5-eos11-eos13, eos2
Network, Ex5-CoreNet-eos1-eos2-eos5-eos11-eos13, eos5
Network, ISP-eos7-eos10-eos19, eos10
Network, ISP-eos7-eos10-eos19, eos19
Network, ISP-eos7-eos10-eos19, eos7
Role, Core, eos1
Role, Core, eos10
Role, Core, eos19
Role, Edge-Router, eos11
Role, Edge-Router, eos13
Role, Edge-Router, eos2
Role, Edge-Router, eos20
Role, Edge-Router, eos5
Role, Edge-Router, eos7
Role, RR, eos1
router_bgp.as, 7, eos1
router_bgp.as, 7, eos11
router_bgp.as, 7, eos13
router_bgp.as, 7, eos17
router_bgp.as, 7, eos2
router_bgp.as, 7, eos5
router_bgp.as, 8, eos10
router_bgp.as, 8, eos19
router_bgp.as, 8, eos7
router_bgp.router_id, 1.1.1.1, eos1
router_bgp.router_id, 10.10.10.10, eos10
router_bgp.router_id, 11.11.11.11, eos11
router_bgp.router_id, 13.13.13.13, eos13
router_bgp.router_id, 19.19.19.19, eos19
router_bgp.router_id, 2.2.2.2, eos2
router_bgp.router_id, 5.5.5.5, eos5
router_bgp.router_id, 7.7.7.7, eos7

## Slide 48: Example5 Device Selection
Enterprise Routing Studio
Campus Studio
EVPN Studio
Interface Configuration Studio

## Slide 49: Example5 Interface Studio Ports
Interfaces Studio
Ethernet 1
Ethernet 6
Apply “Trunk” profile to these ports. See slide 15

## Slide 50: Example5 Traffic Test
From Campus switch eos12 ping DC end device eos9 15.15.15.133 and eos20 15.15.15.134
From Campus switches eos12, ping to eos10 10.10.10.10 and eos19 19.19.19.19 on the ISP Network
From Campus end devices eos9 and eos20, ping to eos10 10.10.10.10 and eos19 19.19.19.19 on the ISP Network

## Slide 51: Example6 OSPF on DC Border Leaf

## Slide 52: Example6 OSPF on DC Border Leaf L3DC has no overlay and mutual redistribution of BGP and OSPF routes.
In this example the Enterprise Routing Studio, consisting of 4 Edge Routers and 2 Core Routers routes a L3DC using L3LS Studio to an L2 DC using the Campus Studio.
On the border leafs on the L3 DC BGP to OSPF redistribution is configured using the Enterprise Routing Studio
Border Leafs are set to the same ASN in the L3LS Studio to prevent routing loops

## Slide 53
Example6 Detail

## Slide 54: Example6 Tags
Campus, L2DC-eos11-eos12-eos13, eos11
Campus, L2DC-eos11-eos12-eos13, eos12
Campus, L2DC-eos11-eos12-eos13, eos13
Campus, L3DC-End-device-eos9, eos9
Campus-Pod, L2DC-eos12, eos12
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos2
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos3
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos4
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos5
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos9
DC-Pod, 1, eos2
DC-Pod, 1, eos3
DC-Pod, 1, eos4
DC-Pod, 1, eos5
DC-Pod, 1, eos9
Edge-Router-Domain, 11-13, eos11
Edge-Router-Domain, 11-13, eos13
Edge-Router-Domain, 2, eos2
Edge-Router-Domain, 5, eos5
Edge-Router-Domain, 9, eos9
Leaf-Domain, 2, eos2
Leaf-Domain, 5, eos5
Leaf-Domain, 9, eos9
Leaf-Number, 1, eos2
Leaf-Number, 2, eos5
Leaf-Number, 3, eos9
Network, Ex6-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos1
Network, Ex6-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos11
Network, Ex6-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos13
Network, Ex6-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos2
Network, Ex6-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos5
Network, Ex6-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos6
Network, L3DC-End-device-eos9, eos9
Role, Core, eos1
Role, Core, eos6
Role, Edge-Router, eos11
Role, Edge-Router, eos13
Role, Edge-Router, eos2
Role, Edge-Router, eos5
Role, Leaf, eos2
Role, Leaf, eos5
Role, Leaf, eos9
Role, Spine, eos3
Role, Spine, eos4
Spine-Number, 1, eos4
Spine-Number, 2, eos3
router_bgp.as, 65000, eos3
router_bgp.as, 65000, eos4
router_bgp.as, 65001, eos2
router_bgp.as, 65001, eos5
router_bgp.as, 65009, eos9
router_bgp.router_id, 1.1.1.1, eos1
router_bgp.router_id, 11.11.11.11, eos11
router_bgp.router_id, 13.13.13.13, eos13
router_bgp.router_id, 172.16.0.1, eos4
router_bgp.router_id, 172.16.0.2, eos3
router_bgp.router_id, 172.16.0.3, eos2
router_bgp.router_id, 172.16.0.4, eos5
router_bgp.router_id, 172.16.0.5, eos9
router_bgp.router_id, 6.6.6.6, eos6

## Slide 55: Example6 Device Selection
Enterprise Routing Studio
Campus Studio
L3LS Studio

## Slide 56: Example6 Traffic Test
From Campus switch eos12 ping DC Leaf eos9 14.14.14.2
From DC Leaf eos9 14.14.14.2 ping Campus switch eos12

## Slide 57: Example7 DC Border Leaf OSPF per VRF

## Slide 58: Example7 DC Border Leaf OSPF per VRF L3 DC has EVPN overlay and runs OSPF on Border Leafs in VRF
In this example the Enterprise Routing Studio, consisting of 4 Edge Routers and 2 Core Routers routes a L3DC using L3LS Studio to an L2 DC using the Campus Studio.
On the border leafs on the L3 DC BGP to OSPF redistribution is configured using the Enterprise Routing Studio
Border Leafs are set to the same ASN in the L3LS Studio to prevent routing loops

## Slide 59
Example7 Detail

## Slide 60: Example7 Tags
Campus, L2DC-eos11-eos12-eos13, eos11
Campus, L2DC-eos11-eos12-eos13, eos12
Campus, L2DC-eos11-eos12-eos13, eos13
Campus, L3DC-End-device-eos9, eos9
Campus-Pod, L2DC-eos12, eos12
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos2
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos3
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos4
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos5
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos9
DC-Pod, 1, eos2
DC-Pod, 1, eos3
DC-Pod, 1, eos4
DC-Pod, 1, eos5
DC-Pod, 1, eos9
Edge-Router-Domain, 11-13, eos11
Edge-Router-Domain, 11-13, eos13
Edge-Router-Domain, 2, eos2
Edge-Router-Domain, 5, eos5
Edge-Router-Domain, 9, eos9
Leaf-Domain, 2, eos2
Leaf-Domain, 5, eos5
Leaf-Domain, 9, eos9
Leaf-Number, 1, eos2
Leaf-Number, 2, eos5
Leaf-Number, 3, eos9
Network, Ex7-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos1
Network, Ex7-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos11
Network, Ex7-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos13
Network, Ex7-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos2
Network, Ex7-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos5
Network, Ex7-CoreNet-eos1-eos2-eos5-eos6-eos11-eos13, eos6
Network, L3DC-End-device-eos9, eos9
Role, Core, eos1
Role, Core, eos6
Role, Edge-Router, eos11
Role, Edge-Router, eos13
Role, Edge-Router, eos2
Role, Edge-Router, eos5
Role, Leaf, eos2
Role, Leaf, eos5
Role, Leaf, eos9
Role, Spine, eos3
Role, Spine, eos4
Spine-Number, 1, eos4
Spine-Number, 2, eos3
router_bgp.as, 65000, eos3
router_bgp.as, 65000, eos4
router_bgp.as, 65001, eos2
router_bgp.as, 65001, eos5
router_bgp.as, 65009, eos9
router_bgp.router_id, 1.1.1.1, eos1
router_bgp.router_id, 11.11.11.11, eos11
router_bgp.router_id, 13.13.13.13, eos13
router_bgp.router_id, 172.16.0.1, eos4
router_bgp.router_id, 172.16.0.2, eos3
router_bgp.router_id, 172.16.0.3, eos2
router_bgp.router_id, 172.16.0.4, eos5
router_bgp.router_id, 172.16.0.5, eos9
router_bgp.router_id, 6.6.6.6, eos6
➜ ~
Notes: Role, Core, eos1
Role, Core, eos6
Role, Edge-Router, eos11
Role, Edge-Router, eos13
Role, Edge-Router, eos2
Role, Edge-Router, eos5
Role, Leaf, eos2
Role, Leaf, eos5
Role, Leaf, eos9
Role, Spine, eos3
Role, Spine, eos4
Spine-Number, 1, eos4
Spine-Number, 2, eos3
router_bgp.as, 65000, eos3
router_bgp.as, 65000, eos4
router_bgp.as, 65001, eos2
router_bgp.as, 65001, eos5
router_bgp.as, 65009, eos9
router_bgp.router_id, 1.1.1.1, eos1
router_bgp.router_id, 11.11.11.11, eos11
router_bgp.router_id, 13.13.13.13, eos13
router_bgp.router_id, 172.16.0.1, eos4
router_bgp.router_id, 172.16.0.2, eos3
router_bgp.router_id, 172.16.0.3, eos2
router_bgp.router_id, 172.16.0.4, eos5
router_bgp.router_id, 172.16.0.5, eos9
router_bgp.router_id, 6.6.6.6, eos6
➜ ~

## Slide 61: Example7 Device Selection
Enterprise Routing Studio
Campus Studio
L3LS Studio
EVPN Studio

## Slide 62: Example7 Traffic Test
From Campus switch eos12 ping DC Leaf eos9 14.14.14.2
From DC Leaf eos9 14.14.14.2 ping Campus switch eos12

## Slide 63: Example8 eBGP Routed Enterprise

## Slide 64: Example8 BGP Routed Enterprise No OSPF or EVPN is used in this example
In this example the Enterprise Routing Studio, consisting of 2 Edge Routers in a Camus, 2 Core Routers and 2 Edge Routers in L3DC

## Slide 65
Example8 Detail

## Slide 66: Example8 Tags
Campus, L2DC-eos11-eos12-eos13, eos11
Campus, L2DC-eos11-eos12-eos13, eos12
Campus, L2DC-eos11-eos12-eos13, eos13
Campus, L3DC-End-device-eos9, eos9
Campus-Pod, L2DC-eos12, eos12
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos2
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos3
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos4
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos5
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos9
DC-Pod, 1, eos2
DC-Pod, 1, eos3
DC-Pod, 1, eos4
DC-Pod, 1, eos5
DC-Pod, 1, eos9
Edge-Router-Domain, 11-13, eos11
Edge-Router-Domain, 11-13, eos13
Edge-Router-Domain, 2, eos2
Edge-Router-Domain, 5, eos5
Edge-Router-Domain, 9, eos9
Leaf-Domain, 2, eos2
Leaf-Domain, 5, eos5
Leaf-Domain, 9, eos9
Leaf-Number, 1, eos2
Leaf-Number, 2, eos5
Leaf-Number, 3, eos9
Network, Ex8-CoreNet-eos1-eos6, eos1
Network, Ex8-CoreNet-eos1-eos6, eos6
Network, L2DC-eos11-eos13, eos11
Network, L2DC-eos11-eos13, eos13
Network, L3DC-Border-Leafs-eos2-eos5, eos2
Network, L3DC-Border-Leafs-eos2-eos5, eos5
Network, L3DC-End-device-eos9, eos9
Role, Core, eos1
Role, Core, eos6
Role, Edge-Router, eos11
Role, Edge-Router, eos13
Role, Edge-Router, eos2
Role, Edge-Router, eos5
Role, Leaf, eos2
Role, Leaf, eos5
Role, Leaf, eos9
Role, Spine, eos3
Role, Spine, eos4
Spine-Number, 1, eos3
Spine-Number, 2, eos4
router_bgp.as, 15, eos11
router_bgp.as, 15, eos13
router_bgp.as, 65000, eos3
router_bgp.as, 65000, eos4
router_bgp.as, 65001, eos2
router_bgp.as, 65001, eos5
router_bgp.as, 65009, eos9
router_bgp.as, 7, eos1
router_bgp.as, 7, eos6
router_bgp.router_id, 1.1.1.1, eos1
router_bgp.router_id, 11.11.11.11, eos11
router_bgp.router_id, 13.13.13.13, eos13
router_bgp.router_id, 172.16.0.1, eos3
router_bgp.router_id, 172.16.0.2, eos4
router_bgp.router_id, 172.16.0.3, eos2
router_bgp.router_id, 172.16.0.4, eos5
router_bgp.router_id, 172.16.0.5, eos9
router_bgp.router_id, 6.6.6.6, eos6

## Slide 67: Example8 Device Selection
Enterprise Routing Studio
Campus Studio
L3LS Studio

## Slide 68: Example8 Traffic Test
From Campus switch eos12 ping DC Leaf eos9 14.14.14.2
From DC Leaf eos9 14.14.14.2 ping Campus switch eos12

## Slide 69: Example9 VRF Lite

## Slide 70: Example9 VRF Lite VRFs are used on the Campus Spline and Enterprise Core routers
In this example the Enterprise Routing Studio, consisting of 2 Edge Routers in a Camus, 2 Core Routers and 2 Edge Routers in L3DC

## Slide 71
Example9 Detail

## Slide 72: Example9 Tags
Campus, L2DC-eos11-eos12-eos13, eos11
Campus, L2DC-eos11-eos12-eos13, eos12
Campus, L2DC-eos11-eos12-eos13, eos13
Campus, L3DC-End-device-eos9, eos9
Campus-Pod, L2DC-eos12, eos12
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos2
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos3
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos4
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos5
DC, L3DC-eos2-eos3-eos4-eos5-eos9, eos9
DC-Pod, 1, eos2
DC-Pod, 1, eos3
DC-Pod, 1, eos4
DC-Pod, 1, eos5
DC-Pod, 1, eos9
Edge-Router-Domain, 11-13, eos11
Edge-Router-Domain, 11-13, eos13
Edge-Router-Domain, 2, eos2
Edge-Router-Domain, 5, eos5
Edge-Router-Domain, 9, eos9
Leaf-Domain, 2, eos2
Leaf-Domain, 5, eos5
Leaf-Domain, 9, eos9
Leaf-Number, 1, eos2
Leaf-Number, 2, eos5
Leaf-Number, 3, eos9
Network, Ex9-CoreNet-eos1-eos6, eos1
Network, Ex9-CoreNet-eos1-eos6, eos6
Network, L2DC-eos11-eos13, eos11
Network, L2DC-eos11-eos13, eos13
Network, L3DC-Border-Leafs-eos2-eos5, eos2
Network, L3DC-Border-Leafs-eos2-eos5, eos5
Network, L3DC-End-device-eos9, eos9
Role, Core, eos1
Role, Core, eos6
Role, Edge-Router, eos11
Role, Edge-Router, eos13
Role, Edge-Router, eos2
Role, Edge-Router, eos5
Role, Leaf, eos2
Role, Leaf, eos5
Role, Leaf, eos9
Role, Spine, eos3
Role, Spine, eos4
Spine-Number, 1, eos3
Spine-Number, 2, eos4
router_bgp.as, 15, eos11
router_bgp.as, 15, eos13
router_bgp.as, 65000, eos3
router_bgp.as, 65000, eos4
router_bgp.as, 65001, eos2
router_bgp.as, 65001, eos5
router_bgp.as, 65009, eos9
router_bgp.as, 7, eos1
router_bgp.as, 7, eos6
router_bgp.router_id, 1.1.1.1, eos1
router_bgp.router_id, 11.11.11.11, eos11
router_bgp.router_id, 13.13.13.13, eos13
router_bgp.router_id, 172.16.0.1, eos3
router_bgp.router_id, 172.16.0.2, eos4
router_bgp.router_id, 172.16.0.3, eos2
router_bgp.router_id, 172.16.0.4, eos5
router_bgp.router_id, 172.16.0.5, eos9
router_bgp.router_id, 6.6.6.6, eos6

## Slide 73: Example9 Device Selection
Enterprise Routing Studio
Campus Studio
L3LS Studio
EVPN Studio

## Slide 74: Example9 Traffic Test
From Campus switch eos12 ping DC Leaf eos9 14.14.14.2

## Slide 75: Example10 Campus EVPN and L3 to the Edge

## Slide 76: Example10 Campus EVPN and L3 to the Edge EVPN is used to Stretch L2 and to segment different user groups
blah

## Slide 77
Example10 Detail

## Slide 78
Example10 Logical Topology

## Slide 79: Example10 Tags
Campus, Site1-Floor1-eos11, eos11
Campus, Site1-Floor2-eos13, eos13
Campus, Site2-Floor1-eos9, eos9
Edge-Router-Domain, End-Device-eos12, eos12
Edge-Router-Domain, External-FW-eos8, eos8
Edge-Router-Domain, FW-Border-Router, eos6
Edge-Router-Domain, ISP, eos7
Edge-Router-Domain, ISP-Border-Router, eos1
Edge-Router-Domain, Internal-FW-eos14, eos14
Edge-Router-Domain, Site1, eos11
Edge-Router-Domain, Site1, eos13
Edge-Router-Domain, Site2, eos9
Edge-Router-Domain, Site2, eos4
Edge-Router-Domain, Site2, eos3
Network, End-Device-eos12, eos12
Network, End-Device-eos16, eos16
Network, Ex10-CoreNet-eos1-eos2-eos3-eos4-eos5-eos6-eos9-eos11-eos13, eos1
Network, Ex10-CoreNet-eos1-eos2-eos3-eos4-eos5-eos6-eos9-eos11-eos13, eos11
Network, Ex10-CoreNet-eos1-eos2-eos3-eos4-eos5-eos6-eos9-eos11-eos13, eos13
Network, Ex10-CoreNet-eos1-eos2-eos3-eos4-eos5-eos6-eos9-eos11-eos13, eos2
Network, Ex10-CoreNet-eos1-eos2-eos3-eos4-eos5-eos6-eos9-eos11-eos13, eos3
Network, Ex10-CoreNet-eos1-eos2-eos3-eos4-eos5-eos6-eos9-eos11-eos13, eos4
Network, Ex10-CoreNet-eos1-eos2-eos3-eos4-eos5-eos6-eos9-eos11-eos13, eos5
Network, Ex10-CoreNet-eos1-eos2-eos3-eos4-eos5-eos6-eos9-eos11-eos13, eos6
Network, Ex10-CoreNet-eos1-eos2-eos3-eos4-eos5-eos6-eos9-eos11-eos13, eos9
Network, FireWalls, eos14
Network, FireWalls, eos8
Network, ISP, eos10
Network, ISP, eos19
Network, ISP, eos7
Role, Core, eos10
Role, Core, eos19
Role, Core, eos2
Role, Core, eos5
Role, Core, eos16
Role, Edge-Router, eos1
Role, Edge-Router, eos11
Role, Edge-Router, eos12
Role, Edge-Router, eos13
Role, Edge-Router, eos14
Role, Edge-Router, eos6
Role, Edge-Router, eos7
Role, Edge-Router, eos8
Role, Edge-Router, eos9
Role, Edge-Router, eos3
Role, Edge-Router, eos4
Role, RR, eos2
Role, RR, eos5
router_bgp.as, 65001, eos14
router_bgp.as, 65001, eos8
router_bgp.as, 904, eos1
router_bgp.as, 904, eos11
router_bgp.as, 904, eos13
router_bgp.as, 904, eos2
router_bgp.as, 904, eos3
router_bgp.as, 904, eos4
router_bgp.as, 904, eos5
router_bgp.as, 904, eos6
router_bgp.as, 904, eos9
router_bgp.as, 10, eos7
router_bgp.router_id, 1.1.1.1, eos1
router_bgp.router_id, 10.10.10.10, eos10
router_bgp.router_id, 11.11.11.11, eos11
router_bgp.router_id, 13.13.13.13, eos13
router_bgp.router_id, 14.14.14.14, eos14
router_bgp.router_id, 19.19.19.19, eos19
router_bgp.router_id, 2.2.2.2, eos2
router_bgp.router_id, 3.3.3.3, eos3
router_bgp.router_id, 4.4.4.4, eos4
router_bgp.router_id, 5.5.5.5, eos5
router_bgp.router_id, 6.6.6.6, eos6
router_bgp.router_id, 7.7.7.7, eos7
router_bgp.router_id, 8.8.8.8, eos8
router_bgp.router_id, 9.9.9.9, eos9

## Slide 80: Example10 Device Selection
Enterprise Routing Studio
Campus Studio
Interfaces Studio
EVPN Studio

## Slide 81: Example10 Interface Studio Ports
Interfaces Studio
Ethernet 6
Ethernet 2
Apply “Trunk” profile to these ports. See slide 15
Ethernet 2
Ethernet 6

## Slide 82: Example10 Traffic Test
From inside GREEN VRF in eos9, eos 11 and 13 ping to ISP 10.10.10.10 and other destinations in GREEN
From inside RED VRF in eos9 and eos13 ping to BLUE end device 1.2.3.12 and other destinations in RED. If E-Tree enabled in RED other destinations in Red should not be reachable except the GW address on the internal FW 3.1.9.1
From inside BLACK VRF on eos11 ping to BLACK 4.3.1.9